Version, 1 March 1995

INTERNATIONAL VAURIEN CLASS

MEASUREMENT FORM

Authority: IYRU, 27 Broadwall, Waterloo LONDON SE1 9PL

1. To obtain a Measurement Certificate, refer to the current class Rules noting particularly that:

(a) 	the Measurement Form must be submitted to the National Authority,

(b) 	the measurer is recognised by the National Authority to measure International Vaurien,

(c) 	the sailnumber has been correctly issued by the International Vaurien Class Association.

Sail number:

Name of builder:

Date of completion:

Constructed of (state materials):

2. General notes for measurers:

(a) 	The boat shall conform to all class Rules, even if some of the Rules are not mentioned on the Measurement Form.

(b) 	If the measurer feels the slightest doubt concerning the accuracy of any part of the boat, he shall report it on the Measurement Form and send it to the National Authority.

(c) 	All measurements are in millimetres unless stated otherwise.

(d) 	Lengths shall be measured parallel to the baseline of the boat, widths perpendicular to the baseline athwartship, heights and depths perpendicular to the baseline in the other direction.

Measurements from transom shall be measured from the plane perpendicular to the baseline and containing the intersection of the transom with the keelline.

(e) 	Masses are in kilograms and are measured by usual weighing scales.

(f) 	Volumes are in cubic metres and areas in square metres.

(g) 	Fittings are in number.

3.	Diagrams

The appended Diagrams form an integral part of the Measurement Form. In the event of an discrepancy between the Diagrams and the Measurement Form, the latter shall prevail.

HULL IN NATURAL POSITION (upright)

No 	Position 	Min	Max

1	Distance between aft side of transom and forward

side of notch in mast thwart 	2705	2735

2	Length overall 	4060	4100

3	Distance between forward side of notch in mast-

thwart and centre of hole forestay fitting 	1175	1185

4	Distance between transom and intersection of

coamings 	3380 	3420

5	Distance between transom and aft side of

centreboard case 	2065 	2095

6	Distance of chainplates for shrouds from transom 	2250 	2320

7	Internal length of centreboard case	350 	360

8	Width of centreboard slot	25 	28

9	Height of upper edge of centreboard case and upper

side of main thwart above of external keel 	324 	334

10 	Beam(from sheerline to sheerline excluding

thickness of rubbing strakes) at transom 	1030 	1050

11 	Beam at section 4	1444 	1464

12 	Beam at section 2	1262 	1282

13 	Distance between transom and aft end of coamings 	2550	2650

14 	Width of deck at transom 	120	140

15 	Width of deck at section 4 	150	170

16 	Width of deck at section 2 	180	200

17 	Width of notch in mast thwart		70

18 	Distance of holes in mast thwart from centreline 	35

19 	Length of mast thwart forward of notch 	70

20 	Depth of mast thwart at notch from sheerline 	11	21

21 	Length of mast thwart aft of the forward leading

edge of the mast notch 1)	100	140

22	Length of main thwart	150

23 	Notches in main thwart and as permitted		4

No 	Position	Min	Max

24	Sidebenches

24a 	Width of side benches	150

24b	Side benches rounding off radius 3)		150

24c	No part of main sheet turning device shall be above

the upper face of side benches 3)	yes	no

25 	Length of side benches 	1060

26 	Depth of side benches from main thwart upper face	0	25

27 	Volume of primary buoyancy apparatus	0,360

28 	Volume of forward buoyancy apparatus	0,100

29 	Volume of secondary buoyancy when necessary 	0,100

30	Dimensions of transom drainage ports:

30a	-minimum diameter	30

30b	-maximum dimension		120

31 	Height of coamings from deck at boats centreline	20

32 	Height of coamings at 50 mm from sheerline	5

33 	Do rubbing strakes comply with dimensions	yes	 no

when placing the template according the paragraph d) of MF4)

34 	Control of stem sections with templates	yes	 no

Templates for checking stem at foredeck and waterline levels will be

complemented by stating minima radii an angles 1)

35 	Height of stem 	505	515

36 	All up mass of a fully rigged boat	95

37	A template 250mm wide with two legs 50mm high over the

cockpit floor checking will be used for checking

this minimum dimension between buoyancy tanks. 1)	250

38	Hull mass 3)

Hull measured with correctors, if any, buoyancy bags, if any

and with all apparatuses and fittings permanently fastened

to the hull, but without spars, rigging, centreboard, rudder

and tiller, sails and sheets 3)	73

No 	Position	Min	Max

41	Centre of gravity 3)

41a)	Percentage of MF no. 38, when the hull is weighed placed

on a triangular section support under section 4 and the stem

placed and a balance (see diagram) 3)	20%

41b)	Percentage of MF No. 38, when the hull is weighed

turned on its side, placed on a support 1000 mm long,

having two legs on the floor at one end and a single keg

on a balance at the other end (see diagram)	22%

46 	Reserved

47 	Correctors if any:

47a	Mass (total)		3

47b	Position (description of location):

47c 	Number	2	2

HULL UPSIDE DOWN

51 	Distance between aft of centreboard slot and aft

side of transom	2015	2045

52 	Distance between stem excluding external keel and transom	4005	4045

53 	Difference (2 - 52)	50	55

54 	Distance between chines in a straightline, at transom	 862	 882

55 	Distance between chines at section 4 	1144	1164

56 	Distance between chines at section 2 	 866 	 886

57 	Distance between keel and baseline at transom 4)	155	155

58 	Distance between keel and baseline at section 4 4)	58 	68

59 	Distance between keel and baseline at section 2 4)	70 	80

60 	Distance between keel and baseline at stem

(excluding external keel) 4)	155	155

61 	Height of chines above keel at transom 	 93	103

62 	Distance between chine and sheerline at transom	224	234

63 	Distance between chine and sheerline at section 4	427	437

64 	Distance between chine and sheerline at section 2	524	534

65 	Tolerance on straight line for measurement 56	 	2

No 	Position	Min	Max

66 	Tolerance on straight line for measurement 62	 	2

67 	Tolerance on straight line for measurement 63	 	2

68 	Tolerance on straight line for measurement 64	 	3

69 	Length of bilge keels	1180

70 	Control of bilge keels with template 3)	yes	no

71 	Control of skeg with template	yes	no

The template used for the control of the skeg will be

complemented by checking the negative tolerance of 5 mm

with a 5 mm wedge. 1)

72 	Control of transom bottom with template	yes	no

73 	Control of external keel 3)

73a	Width of external keel against hull bottom 3)	52	86

73b	Width of external keel bottom face 3)	32

73c	Depth of external keel 3)	28

74 	Control of exposed edge rounding off radius		6

CENTREBOARD

101	Thickness	18

102	Fairing			80

103	Does centreboard comply with dimensions?	yes	no

RUDDER AND RUDDERBLADE

111	Thickness	 18 	22

112	Fairing			80

113	Does rudder comply with dimensions?	yes	no

114	Distance of fore part of rudderblade from transom 4)	30 	40

115	Is the intersection of the leading edges of

the rudder blade level with the water-line (CWL) 4)? 	yes	no

116	Control of fixing of rudderblade in downwards

position 	yes	no

No 	Position	Min	Max

MAST

150	The lower edge of mast thwart measurement band no 1

can not be higher than the upper face of the

mast thwart.

151	Overall height 	 	6300

152	Cross section dimensions 	46

153	Height of upper edge of measurement band no 2 above

lower edge of mast thwart measurement band no 1	 606 	 606

154	Height of spreaders above lower edge of mast

thwart measurement band no 1 	2179 	2233

155	Height of shroud and forestay fixing point above lower edge of

mast thwart measurement band no 1     3)	4106	4149

156	Distance of spinnaker halyard turning point from fore face of mast		100

157	Height of spinnaker halyard turning point on mast

front above lower edge of mast thwart measurement

band no 1	4130	4222

158	Distance between upper edge of measurement band no

2 and lower edge of measurement band no 3	 	5100

159	Maximum distance without groove above upper edge of

measurement band no 2	 	 300

160	Distance of spinnaker boom fitting from foreface

of mast	 		40

161	Mass of mast fully rigged (metallic only) .	 7

RIGGING

171	Is running rigging outside the mast? 	yes	no

172	Diameter of shrouds and forestay

172A 	-Stainless 	 2,5

172B 	-Galvanised	 3

173	Diameter of wire rope halyards 	 2,5

174	Distance of highest halyard guiding conduit from

lower edge of mast thwart measurement band no 1	 	3400

No 	Position	Min	Max

BOOM

181	Overall length 		2600

182	Cross sectional dimensions:

182A 	-Width 		32

182B 	-Height including groove or track 		90

183	Distance between prolongation of aft side of mast

and inner edge of measurement band		2200

184	Distance of aftsheet block fitting aft from inner edge of

measurement band2)	300

SPINNAKER BOOM

191	Overall length		1600

192	Cross sectional dimensions at mid-length	25

193	deleted 4)

MAINSAIL

201	Length of leech (AE')	5280	5330

202	Mid-height radius (CC')		1385

203	Distance IJ, measured as the chord of the sail folded along IJ		4050

204	Length of sail batten pockets:

204A 	-Upper 			 520

204B 	-Middle			 770

204C 	-Lower 		 	670

205	Width at top 		105

206	Control of panel number		 8

207	Control of numbers and emblems 	yes	no

208	Control of sailbatten pocket positions 	yes	no

209	Control of leech (hollow)	yes	no

210	Control of boltrope diameter 	 7

211	Control of luff and foot boltrope start from tack		300

212	Control of construction details 	yes	 no

No 	Position	Min	Max

HEADSAIL

221	Length of leech (FH')	3100	3160

222	Length of luff(FH) 	3580	3650

223	Width of foot (HH')	1570	1600

224	Width of mid-height (GG')		 810

225	Width of material at top 		25

226	Length of middle fold (FK) 		3465

227	Shape of foot: Is any part of headsail foot more

than 10mm from a uniform curve when measured

in accordance with Plans? 1) 	yes	no

228	Control of panel number		 5

229	Control of construction details	yes	no

230	Control of window:

230A 	Area of window 		0,3

230B 	Distances to leech, luff and foot	150

SPINNAKER

241	Length of folded leech(P'Q')	1750 	1800

242	Length of folded centreline (PQ) 	1800 	1850

243	Width of folded sail at mid-height(PP') 	1320 	1350

244	Width of folded foot (QQ') 	1220 	1250

245	Control of panel number		5

246	Control of numbers 	yes	no

247	Control of construction details	yes	no

FITTINGS

301	Chainplates or similar for shrouds and forestay	 3 	 3

302	Chainplates or similar for main sheet at transom 	 2 	 4

303	Fairleads	 2

304	Cleats or similar	 2 	 3

305	Sheaves, single or assembled in blocks 4)	 4 	16

No 	Position	Min	Max

306	Reserved

307A 	Cleats (clam and/or moveable with or without conduit)	 4 	13

307B 	id. if a ratchet block is used 	 2 	11

308	Toe straps 	 2

309	Transom drainage ports 	 1 	 2

310	Compass		 1

311	Self bailers 		 2

321	Pintles and/or gudgeons on transom and rudder	 4	 4

322	Downward fixing device for rudder blade	 1

323	Fixing device for tiller 	 1

324	Lifting device for centreboard 		 1

325	Row locks		 2

331	Gooseneck	 1	 1

332	Spreaders with fittings		 2

333	Fitting for spinnaker boom on foreface of mast 	 1	 1

334	Kicking strap on mast and boom 	 1	 1

335	Outhaul for mainsail on boom 		 1

336	Spinnaker boom end fittings	 2	 2

337	Spinnaker boom middle fitting	1	 1

338	Hooks			 7

339	Swivels			 4

340	Sheets	 	2

341	Lever			 1

342	Spinnaker containers 		 2

1) Changed to 01. March 1992

2) Changed to 01. March 1993

3) Changed to 01. March 1995